## Slide 1: Full-bar Signal: A Wi-Fi AP Positioning System App
Done by:
Sewar Gharaibeh
Rufaida Altalahmeh
Nagham Al-Zoubi
Aya Al-Antari
Supervised by:
Dr. Ahmad Al-Hammouri
Dr. Fahed Awad
Network Engineering and Security Jordan University of Science and Technology

## Slide 2: Outlines
- Introduction
- Smart WiMAP Tool: A brief history
Smart WiMAP vs Full-bar Signal -
- Full-bar Signal Application Process
- Testing
- Throttling
Demonstration -
Conclusion -
- Scanning Test
- Full-bar Signal and Smart WiMAP Test

## Slide 3: INTRODUCTION
What is Full-Bar Signal?
- Optimal AP locator
- Generates heatmap
- Written in Java
- Supports most Android devices
- Easy steps

## Slide 4: Smart wImap: a brief history
Unix-based tool, written in Java
AP locater
Heatmap generation
Rogue AP detection

## Slide 5: Smart WiMAP vs Full-bar Signal
 | OS | Tool goal | Scanning Method
Full-bar Signal | Android | Finding the optimal AP location | Active Scanning
SMART WIMAP | Linux | Showing the coverage heatmap | Passive Scanning

## Slide 6: Active scanning VS passive scanning
Active scanning :
The device initiates the scan
  Advantages
    More accurate results
    User Control
  Disadvantages
    Increased power consumption
    Increased Network Traffic
Passive scanning:
The device acts like listener
  Advantages
    Lower power consumption
    Faster scan time
  Disadvantage
    The device needs to be rooted in Android

## Slide 7: Full-bar Signal APPLICATION PROCESS
Main Activity
MAP Activity
Heat MAP

## Slide 8: FULL-BAR SIGNAL APPLICATION PROCESS
MAIN ACTIVITY​
Scanning network information​.
Choose user's AP​.

## Slide 9: FULL-BAR SIGNAL APPLICATION PROCESS
MAP ACTIVITY
Part1:
Uploading Map Image.
Taking the Required Number of Samples.
Calculating Environment Characteristics Parameters.
  N(Path Loss Exponent) and Sigma(Signal Variation).
Part2:
Choose Optimal AP Location between Given Suggestions.

## Slide 10: FULL-BAR SIGNAL APPLICATION PROCESS
Heat MAP
Inverse Distance Weighting (IDW) algorithm.
Transition between the different heat maps through click on SHOW HEAT MAP button.

## Slide 11: THROTTLING
It involves restricting the frequency of Wi-Fi scanning to enhance network performance, improve security, and extend battery life.
It is evident that the utilization of throttling results in a higher number of scans conducted and an increased scan rate, as compared to the scenario without throttling.
Device Type | Android Version | Scan Rate (scan/s) | 
 |  | Throttling ON | Throttling OFF
Samsung Galaxy A53 | 13.0 | 0.02 | 0.31
Samsung Galaxy A7 | 10.0 | 0.04 | 0.75
Below is a table illustrating the contrast in scanning rates when Throttling is enabled and disabled.

## Slide 12: SCANNING TEST- part1
Group # | Device Type | Android Version | Scan Rate
Group 1 | Samsung A53 time1 | 13 | 0.31/sec
 | Samsung A7(1) time1 | 10 | 0.75/sec
Group 2 | Samsung A52 | 13 | 0.46/sec
 | Samsung S21 | 13 | 0.93/sec
Group 3 | Samsung A31 | 12 | 19/sec
 | Infinix HOT12 time1 | 12 | 15.4/sec
 | Infinix HOT12 time2 | 12 | 17/sec
Group 4 | A7(1) time2 | 10 | 0.7/sec
 | A7(2) time2 | 10 | 0.79/sec
The table below illustrates the close rates observed across devices within a shared environment when the Throttling option is turned off. Each group of devices represents the testing process conducted in the same environment.

## Slide 13
SCANNING TEST- PART 2
We tested the same seven devices on one AP in the university library and the scan rate was nearly identical. It ranges from 1 scan/sec to 1.5 scan/sec.
The investigation on using Wireshark on monitor mode
When testing in monitor mode using (for loop and throttling off) .The time between the probe requests is around one second.

## Slide 14
SCANNING TEST- PART 2 cont.
And the time between the probe request and reply is around 0.004/sec
We solve this problem (different scan rates) by making the user stand in the same point until we gather the required number of samples.

## Slide 15: EFFECT OF THE NUMBER OF SAMPLES AND AP PLACEMENT
AP Location --> in the corner of the testing area
# of samples --> 19 samples
Result: path loss exponents (n) equal 1.64
Test 1

## Slide 16: EFFECT OF THE NUMBER OF SAMPLES AND AP PLACEMENT cont.
AP Location --> at the center
# of samples --> 53 samples
Result: path loss exponents (n) equal 2.32
Test 2

## Slide 17: TESTING RESULTS
The outcome of the testing conducted at the CH building within JUST University is as follows:
 | Smart-WiMAP | Full-bar Signal
Map Scale (meters: pixels) | 1:74 | 1: 64
Path Loss Exponent (n) | 2.27 | 2.32
Greater accuracy in the Smart-WiMAP due to:
finger thickness
  Mouse clicks for selection when selecting two points on the map to enter their real distance in meters, whereas the Full-bar Signal relies on finger taps.
Average RSSI:
  Smart-WiMAP tool takes an average of 10 RSSI readings, the full-bar signal application takes the average of only 3 RSSI readings due to its scanning limitation capabilities in active scan.

## Slide 18: DEMo

## Slide 19: THANK YOU! Any questions?